## Slide 1
TOPIC:Loading constant,Conditional
Exercution and Introduction To
Thumbinstructions
Presented by: LUCA STEVEN MBOGO
Date: 30/05/2025
LS
by Lucia Steven

## Slide 2
Presentation Objectives
Loading Constants
Understand how constants are loaded in ARM architecture.
Conditional Execution
Learn how conditional execution works in ARM.
Thumb Instruction Set
Get introduced to the Thumb instruction set and its significance.

## Slide 3
Loading Constants in ARM
Loading constants involves placing a fixed value into a register for computations, memory access, or control flow. This process initializes registers with known values using specific instruction formats.
Example of Instruction format are:
MOV
Used for small constants (8-bit immediate).
MOV R0, #0xFF ; Load small constant
LDR-Load Register
Used for large constants via literal pools.
LDR R1, =0x12345678 ; Load large constant
MVN
Loads the bitwise NOT of a constant.
MVN R0,#0 ;R0=0’
ADR-Address Relative
Loads the address of a label.
ADR R0,data ;R0=address of data

## Slide 4
Conditional Execution in ARM
ARM allows almost every instruction to be executed conditionally based on flags, specified by a two-letter suffix (e.g., EQ, CC). This minimizes branching, reduces pipeline stalls, and improves performance by avoiding jump instructions, leading to more compact code.
-After arthmetic or Logical Instruction, the following flags set;
N (Negative)
Result is negative.
Z (Zero)
Result is zero.
C (Carry)
Unsigned overflow.
V (Overflow)
Signed overflow.

## Slide 5
Common ARM Condition Codes
Suffix
Meaning
Condition Description
EQ
Equal
Z == 1 (Result was zero)
NE
Not Equal
Z == 0 (Result was non-zero)
GT
Greater Than
Z == 0, N == V (Signed result > 0)
LT
Less Than
N != V (Signed result < 0)
AL
Always
Default (unconditional)

## Slide 6
Conditional Instructions
CMP R0,#10 ; Compare R0 to 10(sets flags)
MOVEQ R1,#1 ;If R0==10,set R1=1
MOVNE R1,#0 ;If R0 !=10,set R1=0

## Slide 7
Introduction to Thumb Instructions
Thumb is a 16-bit instruction set, a subset of the ARM 32-bit instruction set, designed to increase code density. Its smaller instruction size allows more code to fit into limited memory, making it ideal for small, embedded processors and improving power efficiency.
Key Characteristics
Instruction size: 16 bits (vs. 32-bit ARM)
Code density: Half the size of standard ARM instructions
Subset of ARM instructions
Simplified instruction format
Why Use Thumb?
Improved Memory Utilization
Efficient for Small Applications
Power Efficiency

## Slide 8
Thumb vs. ARM Instruction Sets
The choice between ARM and Thumb instruction sets depends on the application's priorities, balancing performance with memory and power efficiency. ARM offers full functionality and speed, while Thumb provides compactness for constrained environments.
ARM (32-bit)
Thumb (16-bit)
FEATURES | ARM Instruction Set(32-bit) | Thumb Instruction Set(16-bit)
Instruction size | 32 bits | 16bits
Code size | Large | Smaller
Performance | Faster excecution (fewer cycles per instruction) | Slower execution(more cycles per instruction)
Instruction Set | Full ARM instruction set | Subset of the ARM instruction
Use case | Performance critical application | Memory constrained applications

## Slide 9
Switching Between ARM and Thumb Modes
Processors can switch between 32-bit ARM mode (default) and 16-bit Thumb mode (for efficiency) using the BX (Branch and Exchange) instruction. The least significant bit (LSB) of the register used with BX determines the target mode.
ARM Mode
Processor uses 32-bit ARM instructions.
BX Instruction
Used to switch modes based on LSB of register.
Thumb Mode
Processor uses 16-bit Thumb instructions.

## Slide 10
-If the Least Significant Bit(LSB)of the register used with BX is 1 ,
The processor will switch to Thumb mode
-If the LSB is 0 , ythe processor will stays in ARM MODE
Example:
BX RO ; If LSB of RO is 0 , ARM mode; if LSB IS 1,Thum mode
ARM (32-bit)
Thumb (16-bit)